## Slide 1: Folding and unfolding of g-spectra

## Slide 2: Unfolding of complex spectra
2

## Slide 3: Not perfect g-detectors
We measure electron energies, not g-rays!
Photo-electric effect
Multi-Compton
Compton
scattering
Pair
production
Back-scattering (Pb)
Threshold

## Slide 4: The problem (I)
incomming
measured
N
E
N
E
e
e
Unfolded u
Raw r
u1
u2

## Slide 5: The problem (II)
Easy to fold
Difficult to unfold
known = r known unknown

## Slide 6: The response matrix
M. Guttormsen et al., NIM A 374, 371 (1996)
Detector response matrix R(E,Eg)
Deposited Eg in detector
Incident energy Eg

## Slide 7: The solution?
Channel by channel
Inverting response matrix R
But large fluctuations in u

## Slide 8: Alternative solution
Exploit that we know how to fold:
Control by iteration:

## Slide 9: Compton subtraction method
The basic principle is that the Compton background is a smoothly varying function, which can be heavily smoothed.
Start with the spectrum from the folding iteration method, u
This can now be used to create the full energy uf, single escape us, double escape ud, and annihilation ua peaks
The Compton spectrum (with backscattering around Eg=200-300 keV) is then uC = r – uf – us – ud – ua
Smooth uC a lot: exp. FWHM
Now, get unfolded spectrum by uunf = = r – uf – us – ud – ua – uC
Finally, correct for full-energy probability pf and detection efficiency e: Uunf = uunf /(pf e)

## Slide 10: Iterations

## Slide 11: Examples of unfolding

## Slide 12: Comparison
Raw
Old
New
Old
smoothed

## Slide 13: Summary
Consistent unfolding and folding
Reduced fluctuations with
Compton subtraction method
M. Guttormsen et al., NIM A 374, 371 (1996)